## Slide 1: higher Design & Manufacture
Metal Processes

## Slide 2: Learning intentions & success criteria
Learning Intentions
Introduction and overview of the metal processes.
Success Criteria
Describe and explain different metal manufacturing processes.
Determine which process certain metal products were produced with.
Determine which process is most suitable for your design.

## Slide 3: Metal Processes
Reforming Processes
  Metal Extrusion
  Gravity Die Casting
  High Pressure Die Casting
  Sand Casting
Deforming Processes
  Piercing/blanking/ press forming
  Drop forging
  Hot rolling/cold rolling
  Spinning
Machining Processes
  Milling
  Metal Lathe

## Slide 4: Metal Extrusion
Molten metal is pushed through a shaped hole
As it passes through the hole, it cools and solidifies
Components which have a long, continuous profile
  Tubes, rods, shaped bars
  Aluminum window frames
  Structural frames for cars or aircraft
Types of metal
  Dies are usually made from steel, therefore metals used must have lower melting point
  Copper is common in water pipes

## Slide 5: Metal Extrusion
Advantages
  Cross section can be extremely complex
  Hollow items can be made
  Different wall thicknesses
  Reinforcing webs can be used to save material
  No marks left like mould lines
  Dimensions can be accurately controlled
Disadvantages
  Molten steel would damage a steel die therefore not possible to make components from steel
  Limitations to overall length depending on how much steel is used in the cross section and the chamber capacity

## Slide 6: Metal Extrusion
The Process (2 methods)
  Method 1
    Direction Extrusion (forward extrusion)
      Uses a ram to push molten metal through a hole in a die
      Once the metal takes the shape of the mould, it cools and solidifies
  Method 2
    Indirect Extrusion
      The ram used in backward extrusion is a hollow tube, which also has the die attached
      As the ram moves forward, the molten metal in the chamber is forces through the hole in the die.
Video: https://www.youtube.com/watch?v=Y75IQksBb0M

## Slide 7: Gravity Die Casting
Process to make solid shapes with a melting point lower than steel
Uses a steel or cast iron two part die
Molten metal is poured in and allowed to cool
Secondary drilling or machining can then be done to complete the part
Products include: car alloy wheels, machinery feet, weights, brackets etc.
Metals used include: aluminium alloys, brass, lead, zinc, magnesium.

## Slide 8: Gravity Die Casting
Advantages:
  Medium to high volume production
  Can be partially automated
  Reasonably good level of surface detail and finish
  Internal stresses kept to a minimum
  Internal tears less likely
Disadvantages
  Excess metal left in the feeder system must be cut off and files before components are completed
  Slow process compared to others
  Thin-walled forms are difficult to achieve

## Slide 9: Gravity Die Casting
The Process
  Stage A
    A mould is made in two parts
    They close to form a mould cavity
  Stage B
    Surface of the mould cavity is treated with powder to help the metal flow
    Mould halves are clamped together
  Stage C
    Metal is heated and poured into the feeder system to fill the cavity
    Mould is tapped or shaken to aid the flow and release gas
  Stage D
    Metal cools and solidifies
    Feeder system is removed
    Excess metal is trimmed and filed
    The mould is removed
Video: https://www.youtube.com/watch?v=xxPLYjqOx9k

## Slide 10: High Pressure Die Casting
Uses a two part steel die
Molten metal is injected under high pressure
It is rapidly cooled
Products can be more intricate than gravity die casting
Metals used: aluminium alloys, brass, zinc, magnesium alloys

## Slide 11: High Pressure Die Casting
Advantages
  High volume production
  Automated process
  High level of detail
  Good surface finish
  Complex shapes
  Metal cools quickly
  Low cycle time
Disadvantages
  Excess metal requires trimming
  Cost of steel moulds is high
  Internal stresses created by high pressure can be great

## Slide 12: High Pressure Die Casting
The Process
  Stage A
    A hydraulic system closes and seals the two die halves
  Stage B
    Molten metal is poured from a ladle into the open injection system
  Stage C
    A ram slowly pushes the molten metal along until it reaches the cavity, slowly to allow gases to escape
  Stage D
    The ram rapidly pushes the metal into the mould, filling the cavity
    Cold water is flushed through channels in the mould which cools the metal
  Stage E
    The hydraulic system opens the mould
    The ram returns to its starting position
  Stage F
    Ejector pins push the component out of the mould
Video: https://www.youtube.com/watch?v=sdO1y0ngDmY

## Slide 13: Sand Casting
Process used to manufacture metal components with complex shapes
Uses sand as a mould into which molten metal is poured and allowed to cool and solidify
Components with holes can be produced
The more complex the shape, the more complex the pattern (solid block which sand is formed around, usually made of wood)

## Slide 14: Sand Casting
Iron is the most common metal
Other include: brass, bronze, aluminium etc.
Advantages:
  Complexity of shape of finished component
  Low cost method of production
  Cost of pattern making is low
  Used with high melting point metals
  Suitable for small scale production
Disadvantages
  Very labour-intensive (sand mould has to be remade each time)
  Further machining of component is often necessary
Video: https://www.youtube.com/watch?v=szOwGvYO_Tc

## Slide 15: Piercing/Blanking/Press Forming
Piercing is process in which a punch operation cuts a hole by tearing material from a final piece of sheet metal.

## Slide 16: Piercing/Blanking/Press Forming
Blanking is a process in which the punch operation removes a final product from a larger piece of sheet metal.

## Slide 17: Piercing/Blanking/Press Forming
Press Forming
  Uses a former to fold sheet metal into shape

## Slide 18: Piercing/Blanking/Press Forming
Types of metal used on all three processes:
  Must be ductile
  Mild steel, stainless steel, aluminium, copper etc.
Advantages:
  Highly automated
  Continuous feeds of material fed into the machine
  Accurate and repeatable
  Scrap can be recycled easily
Disadvantages
  Leaves distinctive marks on the edge of components
  Work hardening can also happen at the edges

## Slide 19: Drop Forging
Uses a powered hammer which hits a heated solid metal blank
This forces it into the shape of the metal die
Used for:
  Items that require a degree of hardness
  Examples: spanners, pliers, screwdrivers, chain links etc
Metals used:
  Titanium, aluminium alloys, stainless steel

## Slide 20: Drop Forging
Advantages:
  Hardening and strengthening of components
  Used on a wide range of components from small jewellery to large truck axles
  Precision drop forging made close to the finished article requires minimum removal of waste
Disadvantages
  Limitations to the shape
  Flash will need to be removed (waste material)
  Difficult to do further machining to drop-forged metal components
Video: https://www.youtube.com/watch?v=VPbJSLE0zic

## Slide 21: Hot Rolling/Cold Rolling
Rolling is the process of deforming metal by squeezing it between a set of rollers
Creates forms like bars or sheets
HOT Rolling:
  Steel billets are heated to soften the steel, making it easier to change shape
  Can be used to make, for example: steel beams
COLD Rolling
  Can be performed on sheet materials which do not need to soften. Carried out at room temperature
  Can be used to make, for example: corrugated roofing
Video: https://www.youtube.com/watch?v=KRn73gKQ2YU

## Slide 22: Spinning
Process by which a disc or tube of metal is rotated at high speed.
This is formed into an axially symmetrical part.
Can be done by hand or by lathe.
Unlike wood turning on a lathe, metal spinning does NOT involve the removal of metal.
It concerns the shaping of a metal sheet over an existing shape.
Complex shapes can be spun.

## Slide 23: Spinning
Process:
  A formed block is mounted on the drive section
  Pre-sized metal disc is then clamped against the block
  They are both rotated together at high speeds
  Force is then applied to the metal using tools
  This forces the metal sheet over the block to eventually take the same shape
Video: https://www.bing.com/videos/search?q=metal+spinning&adlt=strict&view=detail&mid=681F361D595D8E85DBB5681F361D595D8E85DBB5&&FORM=VRDGAR

## Slide 24: Milling
Machining process which uses rotary cutters to remove material
Cutter can move in several directions as well as at an angle
Can be used for a wide range of part sizes
Cutting occurs on the circumference of the cutter rather than a normal drill’s rotational axis
Video: https://www.youtube.com/watch?v=gbjzfE4JA3g

## Slide 25: Metal Lathe
Used to make cylindrical components from metals
The metal is held firmly and is rotated whilst a single-point cutting tool cuts the work using a wedge-cutting action
The shape of the work depends on the path taken by the tool
Video: https://www.youtube.com/watch?v=tRCirIcamVU

## Slide 26: Past Paper question

## Slide 27: Past Paper Answers