## Slide 1: higher Design & Manufacture
Wood processes

## Slide 2: Learning intentions & success criteria
Learning Intentions
To develop an understanding of the properties and uses of Wood in everyday objects.
Success Criteria
I can name 3 common wood processes.
Give examples of there possible uses.

## Slide 3: Wood processes
Here are a few common processes you need to know about:
Laminating
Routing/Spindle Mould
Turning

## Slide 4: Laminating
Laminating (sometimes called glulam) is the process of gluing strips of wood together to form large sections
Can be used to build furniture or building structures
Can be used for most natural timbers and some manmade board such as chipboard

## Slide 5: Laminating
Advantages:
  Allows for much larger timber sections to be created than grow naturally
  Cross section can be varied, allowing thicker parts where more strength is required
Disadvantages:
  Can be very time-consuming to manufacture

## Slide 6: Laminating
Process
  Sections of timber are cut out and glued edge-to-edge
  PVA glue is most commonly used
  Fast-setting adhesives can be used in industrial scale production
  Glued sections are then cramped together until the glue dries
  Sections can then be cut to shape
  For curved shapes, a former must be used
  Components are usually made longer than required and later trimmed
Video:
https://www.youtube.com/watch?v=TK_v01nqWTc

## Slide 7: Routing & spindle mould
Uses a cutter which rotates at high speed to cut grooves or edge details in timber or manmade boards
Cutters can have different profiles to cut different grooves or edge styles
ROUTER: the work piece is fixed and the cutter moves
SPINDLE MOUND: this is fixed in place and the work piece is passed across the cutter (used for long straight work pieces)
Videos:
CNC Router: https://www.youtube.com/watch?v=vS3yILFOqAM
Spindle Mould: https://www.youtube.com/watch?v=z8m57FtK47w

## Slide 8: turning
Used to manufacture item by spinning wooden blanks on a lathe
The blank is then shaped using a variety of tools to produce items with an axis of rotational symmetry
Products include:
  Vases
  Banisters
  Spindles
  Handles
  Bowls
  Chess pieces

## Slide 9: turning
Hardwoods give a better result and finish than softwoods
Irregular grain structure of hardwoods makes more interesting and aesthetically pleasing patterns
More intricate shapes can be made due to hardwood density
Examples of common woods used are:
  Beech
  Elm
  Yew
  Ash
Videos: https://www.youtube.com/watch?v=Nckqhfxabvs

## Slide 10: Past paper question

## Slide 11: Past paper answers